## Slide 1: Project Components
Overall Objectives of the Project:
COMPONENT-1: Inception report (Finalization of methodology and Work Plan)
COMPONENT-2: Detailed Literature Review and its summery and lessons learnt;
COMPONENT-3: Development of input datasets for models of the long-term physical processes
COMPONENT-4: Modeling of the long-term physical processes in the coastal zone;
COMPONENT-5: Finalization of approach for reconstruction of the Polder at different coastal zones including their phasing and construction program;
COMPONENT-6: Updating of design parameters and specifications for planning & design works; review of approaches for management of polders with active participation of beneficiaries and stake holders;
COMPONENT-7: Investment plan for the entire CEIP;
COMPONENT-8: Action plan for Capacity Building of concerned professionals and relevant stake holders in planning, design and management of the polders.
COMPONENT-9: Outreach and communication strategy
COMPONENT-3: Development of input datasets for models of the long-term physical processes

## Slide 2: Componenet-3 - Objective
Componenet-3: Objective
Development of an Interactive Polder Database System for Research, Monitoring, and Analyses of Bangladesh Coastal Zone towards long term sustainable polder development and management with attention to geo-morphological, environmental, economic and ecological aspects.
The database will help in long-term monitoring of polder situation after any project intervention:
Status of physical features (polders/embankments, cannel/channels, protective works, hydraulic structures etc.
Land use Change
Hydro-morphological Change
Change of Socio-Economic scenarios
  Agricultural
  poverty levels,
  education and communication facilities etc.

## Slide 3: Coastal Region Of Bangladesh
710 Km Coastline
35,000 Km2 (approx.)
62% <3m elevation
83% within 5m elevation
32% of land hosts 28% of population (42 Million)
Source: Project Inception Report
Polder Location Map

## Slide 4: IGDCZ-Database Contents
General Admin Boundaries
  Division
  District
  Upazila
  Union
BWDB Boundaries
  Zone
  Circle
  Division
  CEIP Project Boundary
Natural
  Rivers
  Bay of Bengal
    BoB Bottom Elevation
    BoB Bottom Contour
    BoB Bottom Surface
  Polder Elevation
    Contour
    DEM
  Salinity Surface
  Soil Lithology
  Wetlands and waterbodies
  Forest
  River (centerline)
  River Polygon
Morphological
  River erosion
  Coastal Erosion & Accretion
  Bathymetry (Coastal and River)
Hydro-meteorological
  Surface water level (Tidal & non-tidal)
  River discharge
  Ground water levels
  Rainfall
  Sediment Observation
  Cyclone Track
Demographic/Socio-economic
  Population
  Literacy
  Cyclone Shelter
Environmental
  Bio-diversity
  Arsenic Contamination in Groundwater
Agriculture
  Agricultural Land Use (Rabi, Kharif-1 & Kharif-2)
Interventions
  Polders
  Embankments
    Embankment
    Embankment Cross-Section
  Hydraulic Structures
  Protective works
  Canals
    Canal/River Cross Section
    River Bathymetry
  Settlement
  Roads, Bridge / Culverts
  BIWTA Navigation Route
Impacts/Model Results (to be included
  Flooding and inundation
  Drought
  Subsidence
Physiography
  Physiographic features from AEZ Map
Land use Change (1990-2020)
Document Archive
Metadata
Total Layers: 52

## Slide 5: IGDCZ Dashboard

## Slide 6: IGDCZ Database
A Web GIS base Interactive Geodatabase for Coastal Zone (IGDCZ) database System has been developing with more than 50 numbers of layers and datasets of physical features, land use, hydro-meteorological, hydro-morphological changes, agricultural and socio-economic and ecological aspects in the Coastal Zone in Bangladesh.
IGDCZ Modules/Features:
User Login Interface
Dashboard
Interactive GIS
Document Archive
Metadata
Download for data export
User Feedback
Tutorial for user manual
List of datasets/layers
Development platform:
GIS Services and GIS Interface: ArcGIS Enterprise Software
Database: Oracle & PostgreSQL
OS: Windows
Front End Tools: HTML5, CSS, JavaScripts, ArcGIS APIs etc.
Backend: Laravel

## Slide 7: Erosion-Accretion of Bank lines (1989-2020)
The coastal area of Bangladesh is morphologically dynamic
Erosion and accretion are very frequent along the coast
LandSat Images were utilized
Image Resolution: 30m
Study used Satellite images captured in dry season
OLI: Operational Land Imager is a remote sensing instrument aboard Landsat 8

## Slide 8: Erosion-Accretion of Bank lines (1989-2020)
Changes were extracted from satellite images of 1989, 1995, 2000, 2005, 2010, 2015 and 2020.
Erosion-Accretion 1989-2020

## Slide 9: Erosion-Accretion of Bank lines (1989-2020)
Area Statistics in Coastal Erosion and Accretion
Year | Total River Area (ha) | Duration | Erosion (ha) | Accretion (ha) | Net Area (ha)
1989 | 7,07,197 | - | - | - | -
1995 | 6,90,649 | 1989-1995 | 25,938 | 43,369 | +17,431
2000 | 7,09,856 | 1995-2000 | 44,133 | 23,428 | -20,705
2005 | 6,96,600 | 2000-2005 | 29,576 | 42,893 | +13,317
2010 | 6,84,863 | 2005-2010 | 28,579 | 38,906 | +10,327
2015 | 6,96,025 | 2010-2015 | 44,494 | 33,544 | -10,950
2020 | 6,89,313 | 2015-2020 | 35,470 | 40,291 | +4,821
- |  | 1989-2020 | 115090 | 132975 | +17,885
Chart: Accretion-Erosion (1989-2020)
| 1989-1995 | 1995-2000 | 2000-2005 | 2005-2010 | 2010-2015 | 2015-2020
Erosion | 25938 | 44133 | 29576 | 28579 | 44494 | 35470
Acretion | 43369 | 23428 | 42893 | 38906 | 33544 | 40291

## Slide 10: Erosion-Accretion of Bank lines (1989-2020)
Duration : 1989-2020
Erosion (ha) : 115090
Accretion (ha) : 132975
Overall

## Slide 11: Satellite Image Classification
Satellite mosaic images of 1989, 2022, and 2020
Satellite/Sensor | Year | Frame | Date of image
Landsat/TM | 1989 | 138-44, 138-45 | 16/03/1989
 |  | 137-44, 137-45 | 09/03/1989
 |  | 136-44, 136-45, 136-46 | 16/03/1989
 |  | 135-45, 135-46 | 14/01/1989
 | 2000 | 138-44, 138-45 | 11/02/2000, 28/03/1999
 |  | 137-44, 137-45 | 28/02/2000, 21/03/1999
 |  | 136-44, 136-45, 136-46 | 13/02/2000, 19/3/2001
 |  | 135-45, 135-46 | 22/02/2000
Landsat/OLI | 2020 | 138-44, 138-45 | 03/03/2019
 |  | 137-44, 137-45 | 30/03/2020
 |  | 136-44, 136-45, 136-46 | 23/03/2020
 |  | 135-45, 135-46 | 16/03/2020
Image Resolution: 30 meter

## Slide 12: Land Use Change
Land Use Changes from 1989 to 2020
Landuse Feature | Area, Hectares |  |  | Overall Changes |  |  | 
 | 1989 | 2000 | 2020 | 1989-2000, Hectares | % w.r.t 1989 | 2000-2020, Hectares | % w.r.t 2000
Agriculture | 239742 | 304543 | 293626 | 64801 | 27.03 | -10917 | -3.58
Exposed soil | 1791445 | 1567108 | 1511258 | -224337 | -12.52 | -55851 | -3.56
Hill area | 855352 | 854853 | 850427 | -499 | -0.06 | -4426 | -0.52
Mangrove | 430701 | 443560 | 440552 | 12860 | 2.99 | -3009 | -0.68
River | 642105 | 646481 | 629299 | 4376 | 0.68 | -17182 | -2.66
Settlement | 540094 | 680458 | 761273 | 140364 | 25.99 | 80815 | 11.88
Water body | 145732 | 167821 | 206611 | 22089 | 15.16 | 38790 | 23.11
All features | 4645171 | 4664825 | 4693046 | 19654 | 0.42 | 28221 | 0.60

## Slide 13: Some Snapshots